## Slide 1: WF on PDSCH rate matching for supporting aperiodic CSI-RS
Samsung, AT&T, CATT, Ericsson, Huawei, HiSilicon, ITL, ITRI, KDDI, LGE, NTT DOCOMO, Qualcomm, …
3GPP TSG RAN WG1 Meeting #87
Reno, U.S.A, 14th – 18th November 2016
Agenda item: 6.2.2.4.1
R1-1613243

## Slide 2: Proposals
For PDSCH rate matching, 2-bit aperiodic ZP CSI-RS resource signaling field is introduced in DL-related DCIs for all TMs.
  AP ZP CSIRS resource configuration is defined without subframe_config
  UE conducts PDSCH rate matching on AP ZP CSIRS at the subframe when the DCI is signaled.
  AP ZP CSI-RS resource signaling field descriptions are
    State ‘0’: No configured AP ZP CSIRS is indicated.
    State ‘1’: The 1st RRC-configured AP ZP CSIRS is indicated to be applied.
    State ‘2’: The 2nd RRC-configured AP ZP CSIRS is indicated to be applied.
    State ‘3’: The 3rd RRC-configured AP ZP CSIRS is indicated to be applied.
  Collision between ePDCCH REs and aperiodic CSI-RS REs is solved by eNB implementation.