## Slide 1: Way forward on performance observation
Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG RAN WG1 Meeting #87 R1-1613265
Reno, US 14th - 18th November 2016
Agenda item: 7.1.5.1

## Slide 2: Background
Agreement
  The channel coding scheme for eMBB data is LDPC, at least for information block size > X
  FFS until RAN1#87 one of Polar, LDPC, Turbo is supported for information block size of eMBB data <= X
    The selection will focus on all categories of observation, including overall implementation complexity, regardless of the number of coding schemes in the resulting solution (except if other factors are generally roughly equal)
  The value of X is FFS until RAN1#87, 128 <= X <= 1024 bits, taking complexity into account
  The channel coding scheme(s) for URLLC, mMTC and control channels are FFS

## Slide 3: Background
CRC is required for all codes to support error detection.
The number of required CRC bits depends on the coding scheme and decoder algorithm used in the evaluations,
Examples:
  LDPC required 16 CRC bits to provide similar FAR as LTE Turbo
  Polar codes with List-4 CRC aided decoding require 26 CRC bits to provide similar FAR as LTE turbo

## Slide 4: Background
Figure shows performance of LTE turbo code with different CRC overhead.
At 400 block size, performance loss is visible and it is significant at higher code rates.
Higher loss can be expected at lower block sizes.
BLER performance for LTE Turbo codes with 6 and 24 CRC bits. (R1-1613264)

## Slide 5: Background
PC-Polar design has a significant performance loss (2-4 dB) when CRC is attached for error detection.
PC-Polar list-8 with and without CRC bits for 100 info block size (R1-1613264)

## Slide 6: Proposal : Observation
Assuming total coded block size = Info block/code rate, BLER performance degrades with CRC overhead at shorter block sizes.
Performance loss is significant at higher code rates.
PC-Polar design has a significant error performance loss (2-4 dB) when CRC is attached for error detection.