## Slide 1: WF on Hybrid CSI Reporting
NTT DOCOMO, LG Electronics, Nokia, Alcatel-lucent Shanghai Bell, Qualcomm, Samsung, Xinwei, ZTE, ZTE Microelectronics
R1-1613282
3GPP TSG RAN WG1 Meeting #87
Reno, 14th - 18th Nov 2016
Agenda item: 6.2.2.4.2

## Slide 2: Background
Working assumption:
Mechanism 1: Hybrid CSI is realized by with one CSI process, support at least CLASS A for the 1st eMIMO-Type and CLASS B with K=1 CSI-RS resource for the 2nd eMIMO-Type
  i1 is reported while CQI and i2 are not reported for the 1st eMIMO-Type (CLASS A)
    FFS: whether RI is reported for CLASS A
  CQI/PMI/RI are reported for the 2nd eMIMO-Type (CLASS B K=1)
At least one more mechanism is supported, to be discussed in RAN1#86
Agreement:
Confirm the working assumption of hybrid CSI

## Slide 3: Proposals
Following additional mechanism should be supported.
  Hybrid CSI reporting with one CSI process, support Class B with K>1 CSI-RS resources for the 1st eMIMO-Type and Class B with K=1 CSI-RS resources for the 2nd eMIMO-Type
    For the 1st eMIMO-Type, CRI is reported
    For the 2nd eMIMO-Type, CQI/PMI/RI are reported
    Total number of CSI-RS resources across 2 eMIMO-Types is limited by Rel. 13 UE capability Kmax.
    Total number of CSI-RS APs across 2 eMIMO-Types is limited by Rel. 13 UE capability Nmax.