## Slide 1
3GPP TSG-RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 6.2.3.2
R1-1613285
Way Forward on DCI for MUST Case 3
ZTE, ZTE Microelectronics, Huawei, HiSilicon

## Slide 2: Observation
Many states in Table 5.3.3.1.5C-2 are either redundant or not usable when interference of MUST exist. For example, the information of OCC for port 7 does not to be signaled since it can be derived implicitly from assistance information.
When one codeword is enabled, four states in Table 5.3.3.1.5C-2 for port 7,8,11,13 are enough for MUST operation. It is unnecessary to use different nscid for one port.
Efficient signaling should be supported.

## Slide 3: Proposal
For DCI formats 2C and 2D, if MUST interference is not present. legacy table 5.3.3.1.5C-2 is used for antenna port(s), scrambling identity and number of layers indication. If MUST interference is present. Table 5.3.3.1.5C-2 is replaced by Table 1 or Table 2.

## Slide 4
Table 1: Antenna port(s), scrambling identity and number of layers indication for MUST
One Codeword: Codeword 0 enabled, Codeword 1 disabled |  | Two Codewords: Codeword 0 enabled, Codeword 1 enabled | 
Value | Message | Value | Message
0 | 1 layer, port 7, nSCID=0 | 0 | 2 layer, port 7-8, nSCID=0 (OCC=2)
1 | 1 layer, port 7, nSCID=1 | 1 | 2 layer, port 7-8, nSCID=1 (OCC=2)
2 | 1 layer, port 8, nSCID=0 | 2 | 2 layer, port 7-8, nSCID=0 (OCC=4)
3 | 1 layer, port 8, nSCID=1 | 3 | 2 layer, port 7-8, nSCID=1 (OCC=4)
4 | 1 layer, port 11, nSCID=0 (OCC=4) | 4 | 2 layer, port 11,13, nSCID=0 (OCC=4)
5 | 1 layer, port 11, nSCID=1 (OCC=4) | 5 | 2 layer, port 11,13, nSCID=1 (OCC=4)
6 | 1 layer, port 13, nSCID=0 (OCC=4) | 6 | 
7 | 1 layer, port 13, nSCID=1 (OCC=4) | 7 | 
8 | 2 layers, ports 7-8 | 8 | 
1 bit are saved compared to legacy Table 5.3.3.1.5C-2,
Note: if only port 7 and port 8 is signaled, OCC =2.

## Slide 5
Table 2: antenna port(s), scrambling identity and number of layers indication for MUST
One Codeword: Codeword 0 enabled, Codeword 1 disabled |  | Two Codewords: Codeword 0 enabled, Codeword 1 enabled | 
Value | Message | Value | Message
0 | 1 layer, port 7, nSCID=0 | 0 | 2 layer, port 7-8, nSCID=0
1 | 1 layer, port 8, nSCID=0 | 1 | 2 layer, port 7-8, nSCID=1
2 | 1 layer, port 11, nSCID=0 | 2 | 2 layer, port 11,13, nSCID=0
3 | 1 layer, port 13, nSCID=0 | 3 | 2 layer, port 11,13, nSCID=1
2 bits are saved compared to legacy Table 5.3.3.1.5C-2
Note: if only port 7 and port 8 is signaled, OCC =2.

## Slide 6
Table 5.3.3.1.5C-2: antenna port(s), scrambling identity and number of layers indication
One Codeword: Codeword 0 enabled, Codeword 1 disabled |  | Two Codewords: Codeword 0 enabled, Codeword 1 enabled | 
Value | Message | Value | Message
0 | 1 layer, port 7, nSCID=0 (OCC=2) | 0 | 2 layer, port 7-8, nSCID=0 (OCC=2)
1 | 1 layer, port 7, nSCID=1 (OCC=2) | 1 | 2 layer, port 7-8, nSCID=1 (OCC=2)
2 | 1 layer, port 8, nSCID=0 (OCC=2) | 2 | 2 layer, port 7-8, nSCID=0 (OCC=4)
3 | 1 layer, port 8, nSCID=1 (OCC=2) | 3 | 2 layer, port 7-8, nSCID=1 (OCC=4)
4 | 1 layer, port 7, nSCID=0 (OCC=4) | 4 | 2 layer, port 11,13, nSCID=0 (OCC=4)
5 | 1 layer, port 7, nSCID=1 (OCC=4) | 5 | 2 layer, port 11,13, nSCID=1 (OCC=4)
6 | 1 layer, port 8, nSCID=0 (OCC=4) | 6 | 3 layer, port 7-9
7 | 1 layer, port 8, nSCID=1 (OCC=4) | 7 | 4 layer, port 7-10
8 | 1 layer, port 11, nSCID=0 (OCC=4) | 8 | 5 layer, port 7-11
9 | 1 layer, port 11, nSCID=1 (OCC=4) | 9 | 6 layer, port 7-12
10 | 1 layer, port 13, nSCID=0 (OCC=4) | 10 | 7 layers, ports 7-13
11 | 1 layer, port 13, nSCID=1 (OCC=4) | 11 | 8 layers, ports 7-14
12 | 2 layers, ports 7-8 | 12 | Reserved
13 | 3 layers, ports 7-9 | 13 | Reserved
14 | 4 layers, ports 7-10 | 14 | Reserved
15 | Reserved | 15 | Reserved