## Slide 1: Wayforward on the number of orthogonal DMRS ports for DL NR-MU-MIMO
Mitsubishi Electric, CATT, Huawei
3GPP TSG RAN WG1 Meeting #87
Reno, 14th - 18th Nov 2016
Agenda item: 7.1.3.2
R1-1613310

## Slide 2: Background: Agreements from RAN1#86bis

## Slide 3: Background: Contributions related to the number of orthogonal DMRS ports for DL MU-MIMO
Scenario dependent, appropriate modes should be chosen depending on the environment/equipment, system level analysis up to 16 orthogonal ports (R1-1612726)
12 or 16 orthogonal ports, system level analysis up to 16 orthogonal ports (R1-1611244)
16 orthogonal ports, target data rate and spectral efficiency achieved at lower SNR at 16-layer multiplexing (R1-1612839)
Observation : Demand for increasing the number of orthogonal ports is mainly driven by density of UEs (in crowded environments, stronger inter-user interference is present which leads to the need for increasing orthogonal DMRS ports beyond 8)

## Slide 4: Proposal
Support the number of orthogonal DMRS ports for DL up to 16
Study the following aspect for the number of orthogonal DMRS ports up to 16 for DL MU-MIMO
  Mapping DMRS in symbols of a slot
Support configurable DMRS location pattern/density in NR with the number of orthogonal DMRS ports up to 16 for DL MU-MIMO