## Slide 1: Way Forward on channel model for rural scenario in NR
Huawei, HiSilicon, CATT, CATR, [CMCC], [ZTE]...
R1-1613312
3GPP TSG-RAN WG1 #87
Reno, US, November 14-18, 2016
Agenda item 7.1.7

## Slide 2: Background
In 3GPP RAN1#86b meeting, there was a discussion on the channel model for rural scenario in NR, as some models are missing for that scenario. The major issue is that in rural scenario, 50% indoor users are assumed while in the agreed channel model (i.e., rural macro (RMa) channel model in M.2135 [1]) no outdoor to indoor (O2I) channel model was defined. In addition, in M.2135 RMa model, there are no elevation parameters, which are welcome in evaluation.

## Slide 3: Background
Sub-models for rural scenario | Alternative 1 (Extending M.2135 with additional models) | Alternative 2 (Reusing TR 38.900)
Pathloss model | M.2135 | M.2135
LoS probability | M.2315 | M.2135
Shadow fading model | M.2135 | M.2135
Delay spread | M.2135 | M.2135
AoD spread | M.2135 | M.2135
AOA spread | M.2135 | M.2135
Shadow fading | M.2135 | M.2135
K-factor | M.2135 | M.2135
Cross-correlations including only 2D LSPs | M.2135 | M.2135
Delay distribution | M.2135 | M.2135
AoD and AoA distribution | M.2135 | M.2135
Delay scaling parameter | M.2135 | M.2135
XPR - mean | M.2135 | M.2135
Number of clusters | M.2135 | M.2135
Number of rays per cluster | M.2135 | M.2135
Cluster ASD | M.2135 | M.2135
Cluster ASA | M.2135 | M.2135
Per cluster shadowing std. | M.2135 | M.2135
Correlation distance in the horizontal plane including only 2D LSPs | M.2135 | M.2135
Penetration loss model | COST 231 based extension with measurement results | In car penetration is from M.2135, and O2I penetration is based on new model (low loss penetration loss model mainly from high frequency measurements)
LSPs for indoor users | FFS | Reuse the LSPs of outdoor users defined in M.2135
ZoA spread | FFS | Reuse the 3D-UMi ZoA spread in TR 36.873
Cross-correlations including 3D LSPs | FFS | Reuse the 3D-UMa cross-correlations in TR 36.873
ZoD and ZoA distributions | FFS | Reuse the 3D-UMa/UMi (Laplacian) in TR 36.873
XPR – std. variance | FFS | Based on measurements around 1.8 GHz in [3]
Cluster ZSA | FFS | Based on analysis without any measurements
Correlation distance in the horizontal plane including 3D LSPs | FFS | Reuse the 3D-UMa in TR 36.873
ZoD spread | FFS | Based on analysis of measurements in [4]
ZoD offset | FFS | Based on analysis without any measurements.

## Slide 4: Proposal
din : uniform random value between [ 0, min(25,d) ] for each link (fully correlated for a certain site, and independent for different sites), d is the distance between UE and TRP.
is 1 when the link is in LOS state, otherwise, it is 0.
Proposal 2: Adopt the following model as large scale part of O2I penetration loss model for indoor users in rural scenario:
PLpenetration(din) = 11.6 + 0.6×din – 5.53×
Proposal 3: Further study the elevation parameters and fast fading parameters for O2I in rural macro channel model based on measurements.
Proposal 1: If extending RMa channel model, the extension should be based on M.2135/TR 36.873 with additional measurement results.