## Slide 1: Way Forward on 2os sPDSCH structure
Ericsson, Huawei, HiSilicon
R1-1613325
3GPP TSG RAN1 #87
Reno, Nevada (US), Nov 14 - 18, 2016
Agenda item 6.2.10.2.1

## Slide 2: Background
In RAN1#86 bis, a list of DL sTTI patterns was agreed for down-selection
It is preferable to have
  a sPDSCH pattern that avoids orphan symbols
  a sPDSCH pattern not spanning over slot boundary to comply with distributed PDSCH resource block allocation and allow slot based sTTI operation together with 2 symbol sTTI operation
  A sPDSCH pattern with CSI-IM positions not overlapping sTTI borders to allow for accurate CSI-IM measurements

## Slide 3: Proposal (1)
sTTI operation is not supported for N_PRB <= 10
Clarification: the DL sTTI length in R1-168500 refers to the RRC configured DL sTTI length
For 2-symbol TTI, the DL sTTI pattern in OFDM symbols per subframe is adaptive to PDCCH region length as follows.
  The PDCCH region length can be obtained with RRC signaling or PCFICH detection
sTTI 1
sTTI 2
sTTI 0
sTTI 3
sTTI 4
sTTI 5
sTTI 1
sTTI 2
sTTI 0
sTTI 3
sTTI 4
sTTI 5
sTTI 1
sTTI 2
sTTI 0
sTTI 3
sTTI 4
sTTI 5
Slot boundary
PDCCH region =1 OS
{3,2,2,2,2,3}
PDCCH region =2 OS
{2,3,2,2,2,3}
PDCCH region =3 OS
{3,2,2,2,2,3}

## Slide 4: Proposal (2)
For PDCCH region = 1OS and STTI 0, decide if sDCI can be transmitted in the symbol(s) after PDCCH region within this sTTI or in the legacy PDCCH region.
  Alt 1: choose PDCCH or sPDCCH by specification
  Alt 2: high layer signaling to configure between PDCCH or sPDCCH