## Slide 1: WF on remaining issues for Retuning
NEC, Ericsson, Intel
3GPP TSG RAN WG1 Meeting #87 R1-1613335
Reno, USA 14th - 18th November 2016
Agenda Item: 6.2.8.1

## Slide 2
Agreement:
Rel-14 UE supporting CE mode A and/or B can indicate how many narrowband retuning symbols it needs.
  Range: {0, 1, 2} symbols
  Default value: 2 symbols
FFS: If the UE indicates it needs 1 symbol for retuning, then:
  When retuning between two PUSCH narrowbands, the guard period is the last SC-FDMA symbol in the previous UL subframe
  When retuning between two PUCCH narrowbands, the guard period is the last SC-FDMA symbol in the previous UL subframe
  When retuning from a PUSCH narrowband to a PUCCH narrowband, the guard period is the last SC-FDMA symbol in the previous UL subframe
  When retuning from a PUCCH narrowband to a PUSCH narrowband, the guard period is the first SC-FDMA symbol in the next UL subframe
It is up to eNB whether and how to take the UE capability into account.
Background

## Slide 3
If the UE indicates it needs one symbol for retuning, then:
  When retuning between two PUSCH narrowbands, the guard period is the last SC-FDMA symbol in the previous UL subframe
  When retuning between two PUCCH resources, the guard period is the last SC-FDMA symbol in the previous UL subframe
  When retuning from a PUSCH narrowband to a PUCCH resource, the guard period is the last SC-FDMA symbol in the previous UL subframe
  When retuning from a PUCCH resource to a PUSCH narrowband,
    if the PUCCH uses a shortened PUCCH format without transmitting SRS, no additional guard period is generated
    Otherwise, the guard period is the first SC-FDMA symbol in the second subframe.
Proposals