## Slide 1: WF on channel codes for NR short block length eMBB data
3GPP TSG RAN WG1 Meeting #87 R1-1613347
Reno, USA, 14th – 18th November 2016
Agenda Item: 7.1.5.1
AccelerComm, Ericsson, Orange, IMT, LG Electronics, NEC

## Slide 2: Background
Agreement at RAN1#86bis:
The channel coding scheme for eMBB data is LDPC, at least for information block size > X
FFS until RAN1#87 one of Polar, LDPC, Turbo is supported for information block size of eMBB data <= X
  The selection will focus on all categories of observation, including overall implementation complexity, regardless of the number of coding schemes in the resulting solution (except if other factors are generally roughly equal)
The value of X is FFS until RAN1#87, 128 <= X <= 1024 bits, taking complexity into account
The channel coding scheme(s) for URLLC, mMTC and control channels are FFS

## Slide 3: BLER performance on first tx

## Slide 4: …at lower BLER

## Slide 5: BLER performance on subsequent tx
1st tx
2nd tx
3rd tx
4th tx

## Slide 6: …at lower BLER
1st tx
2nd tx
3rd tx
4th tx

## Slide 7: Observations
Enhanced turbo (MLM-8) has similar complexity to LTE turbo (MLM-8), which is widely implemented
Enhanced turbo (MLM-8) offers superior BLER to LTE turbo (MLM-8)
Enhanced turbo (MLM-8) offers superior BLER to polar (SCL-8)
Enhanced turbo (MLM-8) offers similar BLER performance as first transmission of rate-compatible PC-polar (SCL-8)
  Initial investigations suggest that enhanced turbo (MLM-8) offers superior BLER performance in subsequent transmissions
Enhanced turbo (MLM-8) has a steeper BLER curve than PC-polar (SCL-8)
Enhanced turbo naturally offers rate compatible IR-HARQ

## Slide 8: Proposal
Turbo code is adopted for information block size of eMBB data <= 1024
Note: if some system design constraints are found during the work item, it may be desirable to revisit the value of 1024