## Slide 1: Summary of offline discussion on remaining issues for PUSCH in UpPTS
CMCC
R1-1613359
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th - 18th November 2016
Agenda item 6.2.7

## Slide 2: List of Remaining issues
Timing of TTI bunding
Number of available symbols for PUSCH in UpPTS
TBS scaling factor
Power control timing
DMRS design
Remaining issues for UL grant timing
HARQ process number

## Slide 3: 1. Timing of TTI bunding
Support both adaptive and non-adaptive HARQ for TTI bundling considering PUSCH in UpPTS
Specify the PHICH timing for TTI bundling as follows
  For scheduled PUSCH transmissions in subframe n, which corresponds to the last TTI in the bundle, a UE shall determine the corresponding PHICH resource in subframe n+k_phich, with k_phich in the following table
  The UE shall upon detection of a PHICH transmission intended for the UE in subframe n-l, adjust the corresponding first PUSCH transmission in the bundle in subframe n+k, with l in the following table
The number of HARQ processes for subframe bundling operation under TDD configuration 2 and 3 is two.
TDD UL/DL Config | DL subframe number n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 |  | 7 | 6 |  |  |  | 7 | 6 |  | 
3 |  | 7 | 6 | 6 | 6 |  |  |  |  | 
TDD UL/DL Configuration | DL subframe number n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 |  | 3 |  | 0 |  |  | 3 |  | 0 | 
3 | 1 |  |  |  |  |  |  | 7 | 0 | 1

## Slide 4: 2. Number of available symbols for PUSCH in UpPTS
For NCP, the number of symbols for PUSCH (including symbols for both data and DMRS) in UpPTS can be 3,4,5,6;
For ECP, the number of symbols for PUSCH (including symbols for both data and DMRS) in UpPTS can be 2,3,4,5;
The number of symbols that are configured for SRS transmission in UpPTS is signaled to UE supporting PUSCH in UpPTS by RRC signalling;
Special subframe with NCP for both DL and UL
Special subframe with NCP for DL and ECP for UL

## Slide 5: 3. TBS scaling factor
For TBS selection for PUSCH in UpPTS, the PRB scaling factor are chosen based on the following table
  Note that the 1 symbol for PUSCH data transmission case refers to the ECP UL with minimum number of symbols for PUSCH
Available SC-FDMA data symbols in PUSCH | 1 | 2 | 3 | 4 | 5 | 6
Scaling factor | 1/8 |  |  | 3/8 |  | 
Special subframe with NCP for both DL and UL
Special subframe with NCP for DL and ECP for UL

## Slide 6: 4. Power control timing
The power control timing for PUSCH in UpPTS for TDD configuration 0-6 follows the following Table
TDD UL/DL Configuration | subframe number i |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | - | 5 | 7 | 7 | 4 | - | 5 | 7 | 7 | 4
1 | - | 6 | 6 | 4 | - | - | 6 | 6 | 4 | -
2 | - | 5 | 4 | - | - | - | 5 | 4 | - | -
3 | - | 4 | 4 | 4 | 4 | - | - | - | - | -
4 | - | 4 | 4 | 4 | - | - | - | - | - | -
5 | - | 4 | 4 | - | - | - | - | - | - | -
6(LSB of UL index=0 for subframe 2/7) | - | 6 | 7 | 7 | 5 | - | 6 | 7 | 7 | -
6(LSB of UL index=1 for subframe 2/7) | - | - | 6 | - | - | - | - | 6 | - | -

## Slide 7: 5. DMRS design
Confirm the following working assumption as agreement
  When DMRS for PUSCH in UpPTS is transmitted in the UpPTS, DMRS is transmitted in the symbol index l=3 for normal CP, and the symbol index l=2 for extended CP.
The UE can be configured by RRC not to transmit DMRS for PUSCH in UpPTS per carrier
  This configuration is a UE capability
  Note1: RAN1 assumes that the power and phase of the PA is not changed between PUSCH in UpPTS and PUSCH in the following UL subframe
  Note2: RAN1 assumes for the above configurations that the UE is configured with Ks=1, is scheduled with the same PRBs in both UpPTS and the following UL subframe on all UL carriers, open loop component in the power control is the same in PUSCH in UpPTS and the following UL subframe, TPC command should not be updated between the UpPTS PUSCH and PUSCH in the following UL subframe, simultaneous PUSCH and PUCCH is not configured, the phase in the PA is kept in the case that there is an empty OFDM(s) between the PUSCH in UpPTS and PUSCH in the following UL subframe, SRS is not transmitted in the PUSCH in UpPTS, UL extended CP is not configured

## Slide 8: 6. Remaining issues for UL grant timing
For TDD UL/DL configuration 0, confirm the following working assumption as an agreement, and this working assumption is also applied to DCI format 4
  Support the following for timing from UL grant to PUSCH
    Change the interpretation of UL index field
      1)MSB=1, LSB=0: UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE, adjust the corresponding PUSCH transmission in subframe n+k, with k given in the following table.
      2)MSB=0, LSB=1: UE shall adjust the corresponding PUSCH transmission in subframe n+7
      3)MSB=1, LSB=1: UE shall adjust the corresponding PUSCH transmission in both subframes n+ k and n+7, with k in the following table
For UL grant to PUSCH timing in TDD UL/DL configuration 6, the LSB=1 in UL index is not allowed for the subframe #9
TDD UL/DL Config | DL subframe index n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 4 | 5 |  |  |  | 4 | 5 |  |  | 

## Slide 9: 7 HARQ process number
If PUSCH transmission in UpPTS is configured, the HARQ process number follows the following table
  Note: Compared with the case for existing HARQ process number, the modifications are:
    For TDD UL/DL configuration 0, 1, 2 and 6, two more HARQ processes are added,
    For TDD UL/DL configuration 3-5, one more HARQ process is added
TDD UL/DL configuration | Number of HARQ processes
0 | 9
1 | 6
2 | 4
3 | 4
4 | 3
5 | 2
6 | 8