## Slide 1: Way forward on the CAS enhancements For: Decision AI: 6.2.4.1.1
Intel Corporation
3GPP TSG-RAN WG1 #87 R1-1613372
Reno, NV, USA, November 14-18, 2016

## Slide 2: Background
With the introduction of CAS-based system information acquisition, it has been identified that MIB acquisition time is increased due to the longer periodicity of CAS transmissions, i.e., 40ms.
The remaining symbols in the center 6 PRB excluding PDCCH/PSS/SSS/PBCH have limited capacity that can be meaningfully used for SI transmission.

## Slide 3: Proposal
The PBCH region in CAS is extended to 8 symbols.
  In the legacy PBCH region, the 1st, 2nd, 3rd, and 4th scrambled information is transmitted in CAS at SFN mod 4 = 0, 1, 2, and 3, respectively.
  In the additional PBCH region, 2nd, 3rd, 4th, and 1st scrambled information is transmitted in CAS at SFN mod 4 = 0, 1, 2, and 3, respectively.
[Extended CP]
[Normal CP]