## Slide 1: WF on sPUCCH formats
Huawei, HiSilicon, Nokia, ASB, [Samsung], CATT, Ericsson, LG Electronics, NTT DOCOMO, [QC] …
3GPP TSG RAN1 #87
Reno, USA Nov 14 - 18, 2016
Agenda Item: 6.2.10.2.3
R1-1613376

## Slide 2: Proposal
At least the following formats should be designed for sPUCCH:
  For sPUCCH supporting up to 2-bit HARQ-ACK and/or SR (if any)
    DMRS based demodulation for 7-symbol sTTI
    DMRS based demodulation for 4-symbol sTTI if supported
    FFS 2-symbol sTTI
  For sPUCCH supporting more than 2-bit HARQ-ACK and SR (if any)
    DMRS based demodulation for all sTTI lengths
FFS on encoding methods
FFS on sPUCCH with channel selection for up to 4-bit HARQ-ACK.