## Slide 1
3GPP TSG RAN WG1 Meeting #87 R1-1613441 Reno, USA, November 14-18, 2016
Agenda item: 7.1.3.3
WF on Type I & Type II CSI Feedback
Huawei, HiSilicon, China Unicom, …

## Slide 2: Background
In RAN1#86bis, the following agreements were made:
NR supports CSI reporting with two types of spatial information feedback
  Type I feedback: Normal
    Codebook-based PMI feedback with normal spatial resolution
  Type II feedback: Enhanced
    “Explicit” feedback and/or codebook-based feedback with higher spatial resolution
  For Type I and II, CSI feedback per subband as well as wideband feedback are supported
  For Type I and II, beam-related feedback can be included

## Slide 3: Proposal
For Type I CSI feedback
  Support dual-stage W1W2 codebook-based PMI feedback, where
    W1 consists of a subset of basis common for all subbands
    W2 consists of coefficients for each subband
      FFS the details of coefficient
For Type II CSI feedback
  Study at least the following CSI feedback schemes
    Channel covariance matrix feedback
      Codebook based feedback, e.g. Hermitian-form codebook
    Linear combination
    Analog CSI feedback