## Slide 1: WF on partial sensing
Samsung, Sequans, ZTE, …
3GPP TSG RAN WG1 Meeting #87 R1-1613465
Reno, Nevada, USA November 14 – 18, 2016
Agenda item - 6.2.1.2.2

## Slide 2: Background
Agreement (RAN1#86):
The specification supports the possibility for a P-UE to use random selection, including at least all P-UEs which do not have sidelink Rx capability
  If a P-UE uses random selection, it shall only pools in which random selection by P-UEs is permitted
  It is up to network configuration whether a pool in which random selection by P-UEs is permitted overlaps with other pools
  The specification supports the possibility to configure pools in which random selection by P-UEs is not permitted
The specification supports the possibility for a P-UE to use partial sensing in a subset of subframes
  Details of P-UE partial sensing are FFS
    V2V sensing-based resource selection is the baseline; strive to define P-UE partial sensing-based resource selection to be as similar as possible to V2V sensing-based resource selection
  FFS whether support of partial sensing is mandatory for P-UEs with sidelink Rx capability
  FFS under what conditions a P-UE that supports partial sensing uses partial sensing
  If a P-UE uses partial sensing,
    details of resource pool FFS

## Slide 3: Proposals
Support of partial sensing is mandatory for P-UEs with sidelink Rx capability;
P-UE supporting partial sensing should be allowed to use random resource selection at least when:
  resource pool allowing random resource selection is (pre-)configured, and,
  the congestion level of the random resource pool is lower than a (pre-)configured threshold;
  Details are FFS.