## Slide 1: WF on V2V support for TDD
Intel, CATT
3GPP TSG RAN WG1 Meeting #87 R1-1613518
Reno, USA, 14th - 18th November 2016
Agenda item – 6.2.1.7

## Slide 2: Background
RAN1#86 agreement
  V2V pool is defined by a repeating bitmap mapped to all subframes except for at least SLSS subframes which are skipped
TS 36.213
  “The set of subframes that may belong to a PSSCH resource pool for sidelink transmission mode 3 or 4 ….. includes all the subframes except those in which SLSS resource is configured”
Observation
  It is not clear whether DL and S subframes are skipped (similar to SLSS) or not in case of TDD shared carrier
  Additional RAN1 WG agreements are needed to support V2V communication in TDD shared carrier

## Slide 3: Proposals
Proposal 1
  In case of TDD shared carrier, DL and S(Special) subframes are skipped similar to SLSS subframes
Proposal 2
  The Pstep parameter is adjusted according to UL-DL configuration
  Pstep_sharedTDD = Pstep*(UL/(UL+DL+S))

## Slide 4: Proposals
Proposal 3
  The following V2V subframe bitmap sizes are supported for TDD shared carrier
    TDD#0: 60; TDD#1: 40; TDD#2: 20, TDD#3: 30, TDD#4: 20, TDD#5: 10, TDD#6: 50 (equivalent of 100 for FDD/dedicated carrier)
    TDD#0: 12; TDD#1: 8; TDD#2: 4, TDD#3: 6, TDD#4: 4, TDD#5: 2, TDD#6: 10 (equivalent of 20 for FDD/dedicated carrier)