## Slide 1: WF on resource allocation for PDSCH with 5 MHz channel bandwidth
ZTE, ZTE Microelectronics, Sequans, Qualcomm, Ericsson, Sony, [Intel], …
3GPP TSG RAN WG1 Meeting #86bis R1-1613537
Reno, USA 14th - 18th November 2016
Agenda Item: 6.2.8.1.1

## Slide 2: Background
For 5 MHz system bandwidth, one or more narrowbands may be occupied by MPDCCH, distributed resource allocation is necessary for PDSCH with 5 MHz channel bandwidth.
For system bandwidth larger than 5 MHz, it is important that the PDSCH resource allocation allows for good coexistence with Rel-13 eMTC UEs. e.g., MPDCCH narrowband(13-18 PRB) occupied by the same UE or other UEs can not be allocated. Distributed resource allocation is necessary.
PRB | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49
NB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 3: Proposal
For Rel-14 BL/CE UE configured with max 5 MHz PDSCH channel bandwidth,
  at least distributed resource allocation is supported.