## Slide 1
WF on RRM measurement quantity
in CONNECTED mode
LG Electronics, Samsung, CMCC
R1-1613569
3GPP TSG RAN1 #87
Reno, USA, 14th – 18th Nov. 2016
Agenda Item: 7.1.2.6

## Slide 2: Background
For L3 mobility based on DL measurement in CONNECTED mode UE:
  At least non-UE-specific DL signals can be used for CONNECTED mode RRM measurement
    FFS UE-specific DL signals for this purpose
  Study the following DL signals for CONNECTED mode RRM measurement
    Option 1: Cell related RS which is carrying Cell-ID (e.g. NR-PSS, NR-SSS)
    Option 2: RS for mobility
      FFS how to associate it with beam-ID and/or Cell-ID
    Option 3: RS for demodulating broadcast channel
    Option 4: A combination of option 1 and 2
    Other options are not precluded
  At least one of cell-level and beam-level measurement quantities is supported for RRM reporting.
    FFS which RRM measurement quantities to define, e.g., RSRP, RSRQ
  Study the following options for RRM measurement quantities to be reported for L3 mobility:
    Option 1: derived per cell (e.g., if multi-beam, as a function of multi-beam measurements)
    Option 2: derived per beam
    Option 3: A combination of option 1 and 2
    Other options are not precluded
FFS for other UE states (if introduced by RAN2)

## Slide 3: Proposal
For L3 mobility in multiple beam operation scenario, following options for RRM measurement quantity in connected mode can be considered,
  Option 1: The quantity is measured on the best received DL signal resource for RRM measurement
  Option 2: The quantity is a sum of quantities measured on best received “N” DL signal resources for RRM measurement
  FFS : value of N,
  FFS: N is fixed in the specification; or can be signaled via RRC signaling on the RRM measurement configuration
  Other options are not precluded.
  Note: a DL signal resource may correspond to a “beam”