## Slide 1
WF on further clarifications on NR-PBCH
LG Electronics, NTT DOCOMO, Inter Digital, [ Qualcomm, SONY]
R1-1613571
3GPP TSG RAN1 #87
Reno, USA, 14th – 18th Nov. 2016
Agenda Item: 7.1.2.2

## Slide 2: Background
Agreements on NR-PBCH in RAN1 #86bis:
  NR defines at least one broadcast channel: NR-PBCH
    NR-PBCH decoding is based on the fixed relationship with NR-PSS and/or NR-SSS resource position irrespective of duplex mode and beam operation type at least within a given frequency range and CP overhead
      FFS: Unlicensed spectrum case
    FFS relationship between NR-PBCH subcarrier spacing and NR-PSS and/or SSS subcarrier spacing
    Following broadcasting schemes to carry essential system information can be considered
      Option 1: NR-PBCH carries a part of essential system information for initial access including information necessary for UE to receive channel carrying remaining essential system information
      Option 2: NR-PBCH carries minimum information necessary for UE to perform initial UL transmission (not limited to NR-PRACH) in addition to information in Option 1
      Option 3: NR-PBCH carries all essential system information for initial access
      Other options are not precluded

## Slide 3: Proposal
Study further NR-PBCH design options with the following clarification
  NR-PBCH is a non-scheduled broadcast channel carrying system information with fixed payload size and predefined in the specification
  In option 1 in the agreements, UL access information is not included while it is included in option 2