## Slide 1: WF on Coding Technique for Control Channel of eMBB
LG, ASB, AT&T, Ericsson, NEC, Nokia, Qualcomm
R1-1613577
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th - 18th November 2016
Agenda item 7.1.5.1

## Slide 2: Observation
TBCC provides better or comparable performance than other coding techniques for the encoder input size in the range of [16] – 100 bits
List decoding can be applied to improve TBCC decoder performance
  Using list decoding or not is up to receiver implementation

## Slide 3: Proposal
  For DCI, tail-biting convolutional code (TBCC) is adopted as a channel coding technique for NR
  For UCI with encoder input size [16]<=K<=100 bits, TBCC is adopted as a channel coding technique for NR
  FFS: enhancements to LTE TBCC including generator polynomials with larger constraint length, lower native code rate