## Slide 1: Calibration Support for Beam Reciprocity Qualcomm, Interdigital, National Instruments, Fujitsu,[Cohere Technologies]
3GPP TSG RAN WG1 #87 R1-1613595
Reno, Nevada, USA, 14th – 18th November 2016
Agenda item: 7.1.3.3

## Slide 2: Background - I
Following definition of beam reciprocity was agreed in last RAN1 meeting [1]
The followings are defined for Tx/Rx beam reciprocity at TRP and UE :
  Tx/Rx beam reciprocity at TRP:
    TRP is able to determine a TRP Rx beam for the uplink reception based on UE’s downlink measurement report on TRP’s Tx beam.
    TRP is able to determine a TRP Tx beam for the downlink transmission based on TRPs uplink measurement on TRP’s Rx beams
  Tx/Rx beam reciprocity at UE:
    UE is able to determine a UE Tx beam for the uplink transmission based on UE’s downlink measurement on UE’s Rx beams.
    UE is able to determine a UE Rx beam for the downlink reception based TRP uplink measurement on UE’s Tx beam.
R1-1610849, “Way forward on definition beam reciprocity”, 3GPP TSG RAN1 86bis, Lisbon, Neveda

## Slide 3: Background - II
If TX/RX beam reciprocity is available at gNB and UE, a good beam pair obtained from DL beam sweep can be used in UL
System does not need to allow full beam sweep in both directions
  Overhead of beam training reduces significantly
If TX/RX channel reciprocity is available at gNB and UE, CSI obtained in one direction can be used in the other link
  Overhead of channel estimation reduces significantly

## Slide 4: Proposal
NR studies calibration techniques to achieve beam reciprocity at UE
  Study self-calibration and over-the-air calibration techniques for beam reciprocity
  Other techniques to achieve beam reciprocity are not precluded
  FFS: Indication of UE’s state of calibration
  FFS: Study calibration techniques for channel reciprocity