## Slide 1: WF on UL grant-free for URLLC
ZTE, ZTE Microelectronics, Huawei, Hisilicon, CATR, Convida Wireless, III, InterDigital, [CATT], …
3GPP TSG RAN WG1 Meeting #87 R1-1613596
Reno, USA, 14th – 18th November 2016
Agenda item: 7.1.4.4
Document for decision

## Slide 2: Background
Agreements:
At least an UL transmission scheme without grant is supported for URLLC
  Resource may or may not be shared among one or more users
    FFS: resource configuration details
  FFS other details of design

## Slide 3: Observation
From the LLS in [R1-1611296]
The performance with resource collision degrades significantly if no advanced receiver or HARQ is applied.
The performance with advanced receiver is similar to that of without collision, which may meet the requirement of URLLC at reasonable SNR region.
From [R1-1611689]
Contention based grant-free transmission with certain data collision and realistic RS detection as well as realistic channel estimation is able to meet the reliability requirement of URLLC within the 1ms latency bound.

## Slide 4: Proposal
For UL URLLC
  Contention-based transmission scheme without grant is supported
  For physical resource configuration
    Opt. 1: randomly selected by each UE from the pre-defined resource pool(s)
    Opt. 2: pre-configured by base station
    Other options are not precluded
    Combination of different options is not precluded
  Companies are encouraged to propose specific mechanism and evaluation to solve resource collision, e.g. Interference cancellation, HARQ