## Slide 1
WF on L1 broadcast control channel
Qualcomm, MTK, …
R1-1613623
3GPP TSG RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 7.1.4.1

## Slide 2: Background
NR supports different slot formats
It is beneficial for UE to know early the format of the current slot
  The option of delivering the information in DCI follows the normal PDCCH processing delay and is not enough for time critical information delivery
It is also beneficial for UE to detect the slot format of the neighbor gNB
  Needs information to be broadcasted instead of unicast

## Slide 3: Proposal
NR supports an L1 broadcast control channel at least for sub6 case (single beam) indicating at least one or more of the following
  Slot format (e.g., DL-centric, UL-centric, etc)
  Reserved resources
  CFI for number of DL control symbols
  Information related to aperiodic CSI-RS transmission
  Other information not precluded
FFS: Detail design of the L1 broadcast control channel
  Where to put the L1 broadcast control channel
    Example: One fixed NR-CCE
  Payload size, coding, CRC added or not