## Slide 1: WF on Aperiodic CSI-RS Resource Selection
Huawei, HiSilicon, Qualcomm
3GPP TSG RAN WG1 #87 R1-1613634
Reno, NV, USA, 14th – 18th November 2016
Agenda item: 6.2.2.4.1

## Slide 2: Background
Conclusion from RAN1#86bis:
3 alternatives are identified:
  Alt1 Reuse A-CSI request field and add more bit(s) if necessary
  Alt2 Reuse CS field (see R1-1610815, R1-1610816)
  Alt3 Add ceil(log2(N))-bit or 2-bit DCI field
Decide between the above 3 alternatives.

## Slide 3: Proposal
For aperiodic CSI-RS resource selection, the existing A-CSI request field is reused with additional B bits
  B = 0, 1 or 2 configured by higher layer signaling
  Each state of the triggering fields corresponds to a set of combination of {CSI process, CSI-RS resource}
    If MACE CE is not used to activate CSI-RS resource for a CSI process, the CSI-RS resource in the {CSI process, CSI-RS resource} corresponds to the aperiodic CSI-RS resource configured by RRC signaling
    Otherwise the CSI-RS resource in the {CSI process, CSI-RS resource} corresponds to the aperiodic CSI-RS resource configured by MAC CE
  The additional B bits are added to the A-CSI request field for DCI formats 0 and 4 mapped onto the UE specific search space given by the C-RNTI