## Slide 1: WF on remaining issues on QCL for eFD-MIMO
LG Electronics, AT&T, CATT, ITL, KT Corporation, Mitsubishi Electric, Nokia, Alcatel-Lucent Shanghai Bell, NTT DOCOMO, Samsung, Xinwei
R1-1613645
3GPP TSG RAN1 #87
Reno, USA, Nov. 14 – 18, 2016
Agenda Item: 6.2.2.4.1.

## Slide 2: Conclusion from email discussion [86b-10] on QCL assumptions

## Slide 3: Proposal
For QCL indication on DMRS to aperiodic NZP CSIRS, in TM10, aperiodic NZP CSIRS can be configured with UEs configured with QCL Type B, where
  UE is not expected that aperiodic NZP CSIRS is indicated in PQI for QCL purpose with DMRS.
For QCL indication on DMRS to multi-shot NZP CSIRS, in TM10, NZP CSI-RS activation/deactivation can be configured with UEs configured with QCL Type B, where
  NZP CSIRS configured for activation/deactivation can be indicated in PQI for QCL purpose, and follow legacy QCL assumption.
    UE is not expected to receive PQI indication regarding the multi-shot NZP CSIRS within X(ms) from the NZP CSIRS activation. FFS on X.
    Note: NZP CSI-RS not configured for activation/deactivation can also be indicated for QCL purpose.