## Slide 1
3GPP TSG RAN WG1 Meeting #87 R1-1613650 Reno, 14th - 18th Nov 2016
Agenda item: 7.1.3.1
WF on DL MIMO transmission schemes for data transmission
Huawei, HiSilicon, NTT DOCOMO, Ericsson, MTK, China Unicom, Intel, Samsung, Qualcomm, LGE, Xinwei

## Slide 2: Background
Support downlink transmission scheme(s) achieving diversity gain at least for some control information transmission
  Exact scheme is for further study.
  Specification support for such transmission schemes, i.e., the scheme(s) may or may not be implemented in spec-transparent manner
  Note: The data/control channel transmission is at least based on DM-RS for demodulation.
DL and UL transmission techniques should be studied to provide robustness against imperfect CSI and mobility
  e.g.) The techniques using a subset of beams/precoders may include beam cycling, beam broadening, etc.
  e.g.) In case of DL and FDD, this technical scope may include semi-open-loop MIMO technique being discussed in LTE eFD-MIMO.

## Slide 3: Proposal
Support at least the following DMRS based DL MIMO transmissions for data in NR,
  Scheme 1: Closed-loop transmission where data and DMRS are transmitted with the same precoding matrix
    Demodulation of data at the UE does not require knowledge of the precoding matrix used at the transmitter
    Note: spatial multiplexing and rank-1 are included
  Scheme 2: Open loop and Semi-open loop transmissions where data and DMRS may or may not restricted to be transmitted with the same precoding matrix
    Demodulation of data at the UE may or may not requires knowledge of the relation between DMRS ports and data layers
    Note: DMRS can be precoded or not precoded
    Study the transmission schemes, e.g., SFBC, Large delay CDD, Layer shifting, small delay CDD
    Study the selection of transparent and/or non-transparent DMRS
      Transparent DMRS: DMRS and data precoded identically
      Non-transparent DMRS: DMRS and data precoded differently