## Slide 1: WF on Support of Small Transmission Periods for V2V Communication
Intel, Qualcomm Inc.
3GPP TSG RAN WG1 Meeting #87 R1-1613655
Reno, USA, 14th - 18th November 2016
Agenda item – 6.2.1.7

## Slide 2: Background
At the RAN1#86bis, the following agreements were made
  FFS the following aspects till the next meeting
    Scale the SL_RESOURCE_RESELECTION_COUNTER to 2(for 50ms period) or 5 (for 20 ms period)
    S-RSSI measurement interval is (select one of the options at the next meeting)
      100 ms interval is kept;
      set to the minimum allowed i;
      set to the resource reservation interval used for transmission of the UE;
      Combination of allowed intervals {20, 50, 100} with shortened averaging duration.
    In step2, reselection UE scales the number of reservations of other UE within selection window by 1/i when 0<i<1.

## Slide 3: Proposal
Apply scale factor of 2 and 5 to resource reselection counter range [5, 15]
Confirm that reselection UE scales the number of reservations of other UE within selection window by 1/i when 0<i<1
For SL-RSSI averaging, averaging period is set to the minimum value of (20, 50 and 100), if those are configured by the system, but is not larger than 100ms