## Slide 1: WF on Multiplexing eMBB and URLLC in DL
Samsung, Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #87
Reno, USA, 14th – 18th November 2016
Agenda item: 7.1.1
R1-1613657

## Slide 2: Background
RAN1#86 Agreements:
  At least the following potential options should be considered
    At least for shorter transmission UL, semi-static resource sharing between URLLC and eMBB
      FDM and/or TDM manner
        UL grant-free transmission for URLLC
        Other schemes are not precluded
    Dynamic resource sharing between URLLC and eMBB
      For DL, mechanisms to schedule a transmission where the resources of it can overlap with resources of ongoing/scheduled longer transmission at least from network perspective
        FFS: A similar or same mechanism applicability to UL
        Preemption or superposition
        Other schemes are not precluded
      Scheduling based approaches (e.g., by adapting transmission duration or by using different subbands) to allow multiplexing of different durations of transmission
      UL grant-free transmission for URLLC
      Other schemes are not precluded
    Other mechanisms are not precluded

## Slide 3: Background
RAN1#86bis Agreements:
  From network perspective, multiplexing of transmissions with different latency and/or reliability requirements for eMBB/URLLC in DL is supported by
    Using the same sub-carrier spacing with the same CP overhead
      FFS: different CP overhead
    Using different sub-carrier spacing
      FFS: CP overhead
    NR supports both approaches by specification
  NR should support dynamic resource sharing between different latency and/or reliability requirements for eMBB/URLLC in DL

## Slide 4: Background
R1-1612538
  Observation 1: If eMBB receiver does not know which region should be punctured, eMBB BLER performance can be significantly degraded. However, if eMBB receiver can be aware of the puncturing regions, eMBB BLER performance can be significantly improved.
  Proposal 1: Study how eMBB receiver knows eMBB puncturing regions in case of preemption-based dynamic resource sharing between eMBB and URLLC.

## Slide 5: Proposal
NR supports URLLC transmission by preemption on eMBB transmission resources.
  Support indication of preempted or impacted eMBB resources to respective eMBB UE(s)
  FFS: Indication can be implicit/explicit
Study how to handle preempted/impacted eMBB data by URLLC
  HARQ retransmission with indication to eMBB UE of symbols and/or PRBs of the previous transmission for the same HARQ process that were preempted/impacted by the URLLC transmission
  Transmission of eMBB data preempted or retransmission of eMBB data impacted by the URLLC UE without HARQ-ACK feedback for previous transmission of eMBB data