## Slide 1: Wayforward on the number of orthogonal DMRS ports for DL and UL NR-MU-MIMO
Mitsubishi Electric, Huawei, Samsung, Ericsson, [CATT], [Softbank], [KDDI]
3GPP TSG RAN WG1 Meeting #87
Reno, 14th - 18th Nov 2016
Agenda item: 7.1.3.2
R1-1613660
(Revision of R1-1613310, R1-1613552)

## Slide 2: Background: Agreements from RAN1#86bis

## Slide 3: Background: Contributions related to the number of orthogonal DMRS ports for DL MU-MIMO
Scenario dependent, appropriate modes should be chosen depending on the environment/equipment, system level analysis up to 16 orthogonal ports (R1-1612726)
12 or 16 orthogonal ports, system level analysis up to 16 orthogonal ports (R1-1611244)
16 orthogonal ports, target data rate and spectral efficiency achieved at lower SNR at 16-layer multiplexing (R1-1612839)
Observation : Demand for increasing the number of orthogonal ports is mainly driven by density of UEs (in crowded environments, stronger inter-user interference is present which leads to the need for increasing orthogonal DMRS ports beyond 8)

## Slide 4: Proposal
Support at least 16-layer MU-MIMO spatial multiplexing in DL and UL using orthogonal and/or non-orthogonal DMRS ports
  Study the following topics:
    Support for up to 16 orthogonal DMRS ports for NR MU-MIMO
    The number of scrambling codes, cyclic shifts for ZC sequences
    Combination of orthogonal DMRS ports with scrambling codes
    Multiple sets of orthogonal DMRS ports: how to achieve semi-orthogonality among the sets is FFS