## Slide 1: WF on two stage DCI design
Huawei, HiSilicon, Qualcomm, OPPO, Convida, ZTE, Fujitsu, Mediatek, InterDigital, Intel
3GPP TSG RAN WG1 #87 R1-1613668
Reno, November 14 – 18, 2016
Agenda item: 7.1.4.1

## Slide 2: Observation
A number of use cases have been identified in [R1-1611656] where two (or multiple) steps DCI transmission could have benefits over single-stage DCI as follows:
  Processing timeline improvement
  Control offloading
  DCI length management and reduction of blind detections
  Reduce the control overhead (e.g. slow first DCI, fast second DCI)
  Easier beamforming control: the first step uses a wider (more robust) beam while the second step uses a narrower beam (same as for data).
  Separate resource allocation and MCS indication in two steps can also be a benefit assuming measurement and measurement reporting can be conducted in between.
  Dynamic change of transmission mode
  Resource adjustment (e.g. eMBB and URLLC multiplexing)
  For transmissions of short duration (such as for URLLC) for which provision of full control information for every transmission would result in excessive overhead
  Forward compatibility: easier extension of the control channel capacity in the second-step DCI

## Slide 3: Proposal
Support two stage DCI design
  At least first step DCI can use the same or different control resource set(s) which is used for single-stage DCI, FFS on alternatives for the time-freq resource of the second step DCI
    Alt1: In a later control OFDM symbol (including the case with a split control OFDM symbol)
    Alt 2: In the PDSCH region (where the resource of PDSCH region is indicated in the first step DCI)
    Other alternatives are not precluded
  FFS on first step and second step DCI in same and/or different slots/mini-slot
  FFS on how to split DCI content between the two stage DCI transmissions
  FFS on the transmission schemes of the two-stage DCI