## Slide 1: WF on CSI-RS for beam management
Samsung, NTT DOCOMO, Ericsson, MediaTek, Intel, CATT, AT&T, InterDigital
R1-1613669
3GPP TSG RAN WG1 Meeting #87
Reno, USA, 14th - 18th November 2016
Agenda item 7.1.3.3

## Slide 2: Background
RAN1#86bis meeting had the following agreement:
  Working assumptions:
  Beam management procedures can utilize at least the following RS type(s):
    RS defined for mobility purpose at least in connected mode
      FFS: RS can be NR-SS or CSI-RS or newly designed RS
        Others are not precluded
    CSI-RS:
      CSI-RS is UE-specifically configured
        Multiple UE may be configured with the same CSI-RS
      The signal structure for CSI-RS can be specifically optimized for the particular procedure
      Note: CSI-RS can also be used for CSI acquisition
  Other RS could also be considered for beam management such as DMRS and synchronization signals

## Slide 3: Proposal
CSI-RS supports the TRP Tx beam sweeping and UE Rx beam sweeping
NOTE: CSI-RS can be used in P1, P2, P3

## Slide 4: Proposal
NR CSI-RS supports the following mapping structure
  NP CSI-RS port(s) can be mapped per time unit
    Here, “time unit” refers to n>=1 consecutive OFDM symbols in reference numerology, where the value of n is FFS
    Beams corresponding to different CSI-RS ports can be to same or different
    FFS Port multiplexing method
  Each time unit can be further partitioned into sub-time units
    FFS Partitioning method, e.g., IFDMA, OFDM symbol-level partition with same/shorter OFDM symbol length(i.e. smaller subcarrier spacing) as/than the reference OFDM symbol length (subcarrier spacing)
  Options to map CSI-RS for Tx and Rx beam sweeping for further study
    Option 1:
      Tx beam(s) are same across sub-time units within each time unit
      Tx beam(s) are different across time units
    Option 2:
      Tx beam(s) are different across sub-time units within each time unit
      Tx beam(s) are same across time units
    Option 3: combination of Alt1 and Alt2:
      Within one time unit, Tx beam(s) are same across sub-time units.
      Within another time unit, Tx beam(s) are different across sub-time units.
      FFS combination of the different time units in terms of e.g., number and periodicity
    Other options are not precluded.
    FFS: how to capture “same beam” and “different beam” in spec
FFS: Whether the above mapping structure is configured with one or multiple CSI-RS resource configurations

## Slide 5: Appendix
Ex.1
Ex.2
Time units
Time units
Sub-Time units
Sub-Time units