## Slide 1
Way Forward on Two-Step RACH Procedure
Nokia, ASB, Mediatek, Ericson
3GPP TSG RAN WG1 #87 R1-1613685
Reno, Nevada, USA, 14th – 18th November 2016
Agenda item: 7.1.2.5

## Slide 2: Background
Agreements:
RAN1 is studying and some companies see potential benefits of a simplified RACH procedure consisting of two main steps (Msg1 and Msg2) for UEs
RAN1 has discussed the following:
  The use of a UE identity in Msg 1
  Msg 2: RA response that is addressed to the UE identity in Msg 1
  FFS on the definition and choice of the UE identity
  FFS on the applicability scenarios of simplified RACH procedure
RAN1 to send LS to RAN2
RAN1 is aware that RAN2 is also studying the RACH procedure and RAN1 would like to inform RAN2 to take the above into considerations and would like to request any feedback on UE identities and associated procedure and also ask the corresponding applicable scenarios

## Slide 3: Way Forward
2-step RACH procedure includes Msg.1(UL) and Msg.2(DL)
  Msg.1 may include a RACH preamble and/or a data signal.
    FFS: Msg.1 consists only of data signal
    FFS: Msg.1 consist only of preamble
  The data signal, if present, is sent in a different time and/or frequency resource than that of preamble.
  Support at least single beam operation
  Study overhead of 2-Step RACH procedure in multi-beam operation

## Slide 4: Way Forward
  Msg.1 preamble, if present, is at least used for:
    UE activity detection
    UL timing alignment detection in case UL sync. is not established or lost.
    FFS: Resources indication of Msg.1 data
    FFS: Reference signal for the data signal.
    FFS: Beam recovery
    FFS: UE identification
    Other uses not precluded.
  Content of Msg. 1 data signal, if present, is determined by RAN2

## Slide 5: Way Forward
  Msg.2 is the random access response/Contention resolution message. Msg.2 carries:
    Content of Msg.2 needed for the RACH procedure would be decided by RAN2.
    Layer 1 related information could include:
      FFS: TA
      FFS: UL grant
      Other information not precluded.