## Slide 1: WF on the frequency selective precoding for UL MIMO
Samsung, Xinwei, NTT DOCOMO
3GPP TSG RAN WG1 Meeting #86bis
Reno, USA 14th - 18th November 2016
Agenda item: 7.1.3.1
R1-1613231

## Slide 2: Background
The following was agreed in RAN1#85:
  The following techniques are studied for NR UL MIMO
    Uplink transmission/reception schemes for data channels
      Non reciprocity based UL MIMO (e.g. PMI based)
      Reciprocity based UL MIMO. E.g. UE derives precoder based on downlink RS measurement (including partial reciprocity)
      Support of MU-MIMO
      Open-loop/Close-loop single/Multi point spatial multiplexing
        e.g. for multi point SM, multi layer is received either jointly or independently by different TRPs
        Note: for multi point SM, multiple point may have coordination
      …
Note: The terms ‘open-loop’ and ‘closed-loop’ spatial multiplexing for UL MIMO
  For DL MIMO in FDD, the terminologies are suitable for categorization
  However, precoding feedback is non-existent for UL MIMO

## Slide 3: Background
The following was agreed in RAN1#86:
  The following aspects for UL MIMO transmission should be supported:
  Transmission schemes/methods for reciprocity calibrated UEs, reciprocity non-calibrated UEs, and non-reciprocity/partial reciprocity cases
    …
  At least one of the following candidate schemes/methods is to be supported
    Candidate 1: Codebook based transmission
      Frequency selective and frequency non-selective precoding in digital domain can be considered for large system bandwidth
        The support for frequency selective precoding is conditioned on decision on NR waveform(s)
        FFS: The values of the large system bandwidth
      …
    Candidate 2: Non-codebook based transmission
      Frequency selective and frequency non-selective precoding in digital domain can be considered for large system bandwidth
        The support for frequency selective precoding is conditioned on decision on NR waveform(s)
        FFS: The values of the large system bandwidth
      …

## Slide 4: Proposal
Replace the classifications ‘open-loop’/’closed-loop’ with method-based classification of ‘precoding’ and ‘precoder cycling’
  Same classification as DL MIMO
  Signalling and UL-CSI measurement support are to be addressed separately
  Both precoding and precoder cycling should be supported for UL DMRS-based spatial multiplexing (SM)
  Note: SFBC is covered by this clarification
Frequency selective precoding is supported for UL MIMO with CP-OFDM waveform
  Example 1: Precoding information for a given partial BW is explicitly indicated by gNB
  Example 2: A single beam group in UL codebook is indicated by BS for UL transmission in perspective of the system bandwidth
    Example 2a: Precoder cycling is adopted within the beam group
    Example 2b: The UE has certain flexibility to decide which particular beam/precoder in the beam group for actual transmission.