## Slide 1: Observation on TBCC LVA and Polar for eMBB small block
Huawei, HiSilicon
R1-1613303
3GPP TSG-RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 7.1.5.1

## Slide 2: Outlines
Background
Calibration
  TBCC LVA & Polar computation complexity formulas
  TBCC LVA & Polar performance
CRC penalty
Observations

## Slide 3: Background
In R1-1612089 (Qualcomm), it is claimed that
  For R=1/3 and 40-bit DCI, the list size for the Polar list decoder needs to be nearly 2x that of the TBCC list decoder to achieve the same SNR for 10e-3 BLER.
  For larger list sizes, TBCC(L=16) and Polar(L=32) begin to have the similar computational complexity and performance tradeoffs.
In this contribution, we align the computational complexity of TBCC and Polar of Huawei and Qualcomm, and compare performance in terms of calculation per information bit

## Slide 4: Computational complexity calibration (TBCC)
 | Component |  | Addition | Comparison
Initial state searching | Branch metric |  | Kt*[min((m-2)*2^(m-1)+1, (m-1)*2*S)] | 
 | Path metric |  | Kt*2S | 
 | sort |  |  | Kt*S
decoding | Branch metric |  | K*[min((m-2)*2^(m-1)+1, (m-1)*2*S)]*Sinitial | 
 | Path metric |  | K*(L-1)*S*Sinitial | 
 | sort |  |  | K*SL*Sinitial
backtrace |  |  | (L*log(L) + KL)*Sinitial | 
Total |  | (Kt+K*Sinitial)*[min((m-2)*2^(m-1)+1, (m-1)*2*S)]+Kt*3S+(K*2SL-K*S + L*log(L) + KL)*Sinitial |  | Kt*S+K*SL*Sinitial
Parameters: K: infolen; / R: Rate, / V: constraint length / S: No. of state; S = 2^(V-1) / L: list size for LVA / m: No. of coded bits per info bit m = 1/R
Kt: training length for initial state searching, Sinitial = No. of initial states
Component | Complexity
Branch metric calculation | 2*K*[min(2^(m+1)-2, m*2*S)]
Trellis development for state determination | S*2*K + S*K
Trellis development for list decoding | S*(L+1)*K + S*L*K
Handling of the final stage and backtrace | L*log(L) + KL
Total | 2*K*[min(2^(m+1)-2, m*2*S)] + 3*S*K + S*(2*L+1)*K + L*log(L) + KL
Huawei: (R1-164040)
Qualcomm(R1-1612089):
Complexity of Qualcomm’s TBCC is Close to Huawei’s while Kt = K, and Sinitial = 1

## Slide 5: Computation complexity calibration (Polar)
Polar SC-List Decoder Component | Complexity (QC,R1-1612089) | Complexity (HW, R1-164040 with frozen header skipping*)
Single Parity Check |  | 
Repetition |  | 
Path Metric Calculation |  | 
Sorting |  | 
Parameters | Number of info bits (containing CRC): K Number of coded bits: N List Size: L R = 0.78 for K=56, N= 120 with PC-Polar, R= 0.56 for K = 200, N=1000 | 
* The computation complexity of Qualcomm’s can be reduced by Frozen- Header-Skipping(R1-164040) without any performance loss, especially for low code rate.

## Slide 6: Performance vs complexity
QC’s performance and complexity* of CA-Polar can be reproduced (blue curve)
QC’s complexity of polar is 20% more than Huawei’s (red curve) due to Frozen- Header-Skipping(R1-164040)
QC’s TBCC calc complexity** is consistent to the table in sec2.1 where training length Kt = K and Sinitial = 1
But the performance of Kt = K can not be calibrated (Green curve performance for Huawei Kt = K and Sinitial = 1)
We reproduce similar Performance with QC’s black curve with Kt = 2K, and Sinitial = 64 (purple curve), but the complexity is much higher (100x +)
*Polar computation complexity is evaluated with formulas in slide5
**TBCC LVA computation complexity is evaluated with formulas in sllide4

## Slide 7: CRC penalty
There are two solution to improve the performance of TBCC LVA decoder
    Increase list size, L
    Try more initial state, Sinitial, for each L candidates
The CRC check number of worst case is L x Sinitial ,which will be 2048 for list32 with full initial state search, thus have huge CRC performance loss.
Thus additional log2(L x Sinitial ) CRC bits need to be added to compensate to CRC penalty
Adopting PC-Polar(R1-1611254) can avoid CRC performance loss with list decoder

## Slide 8: Observations
Complexity of Qualcomm’s TBCC is Close to Huawei’s while Kt = K, and Sinitial = 1
Complexity of Qualcomm’s Polar is ~20% larger than Huawei’s for the DCI case K=56,N=120, due to Frozen- Header-Skipping
The complexity of TBCC LVA is much larger than that of Polar with same list size, even with training length Kt=K.
The performance of TBCC LVA is not competitive with Kt = K, and Sinitial = 1.
The performance of TBCC LVA can be improved by increasing Sinitial , which will increase the computation complexity and further lead CRC performance loss.
TBCC LVA computational complexity and performance tradeoffs is much worse than that of Polar list decoder.