## Slide 1: Way Forward on Hardware Efficiency for a 2-code eMBB Data Channel
Huawei, HiSilicon, AccelerComm, Alibaba, CATR, CATT, Coolpad, CMCC, China Telecom, China Unicom, Hytera, IMT, LG Electronics, Lenovo, MediaTek, Motorola Mobility, Neul, Nubia Technology, OPPO, Orange, Potevio, Spreadtrum, SRTC, Starpoint, TD-Tech, Turk Telekom, Vivo, Xiaomi, Xinwei, ZTE, ZTE Microelectronics
R1-1613306
3GPP TSG-RAN WG1 #87
Reno, USA, 14th – 18th November 2016
Agenda item 7.1.5.1

## Slide 2: Observations
Contributions from companies raising concern on the power / area efficiencies and performance of a LDPC-only flexible decoder…
R1-1611319 (Ericsson)
  "On the other hand, adopting LDPC-only for eMBB data is not as efficient with hardware implementation as Option 1. Compared to covering the high info block sizes only, it is more challenging to design an LDPC decoder to cover the full range of code sizes and code rates of eMBB.“
R1-1612280 (Nokia)
  About LDPC channel code .. “In general, flexibility and implementation efficiency (considering higher throughputs and energy efficiencies) are two conflicting goals. Higher flexibility can be provided at the expense of area and energy efficiencies”
R1-1611259 (Huawei)
  Small codeword decoding performance suffers from larger area complexity of flexible decoder
R1-1612306 (Accelercomm)
  At low R and small N, flexible LDPC decoder has degraded area and energy efficiencies

## Slide 3: Observations
2-code solution with optimized decoders provides :
  Better computational efficiency with higher hardware resource utilization
    In contrast to LDPC channel code, Turbo and Polar decoder can leverage all of their computation resources for small info block sizes (with info bits up to 1024 bits) and all code rates
  Power efficiency with better channel code for small info block sizes
    More LDPC iterations are required at small info block sizes and consumes more energy
    More specialized decoder are required to improve BLER performance at additional implementation complexity.
 2-code solution emphasizes the strength of each code and mask the disadvantages of the other code.

## Slide 4: Observations
More energy saving in a 2-code solution compared to single-code Flexible LDPC solution
  In a 2-code solution, only one decoder is active at the time
    The other decoder remains inactive without dynamic power consumption
  R1-1612085 (Qualcomm)
    For small info blocks decoding, 100% of the permutation network is active
      From table 3, QSN area is >= 50% of decoder logic
      QSN area is under-estimated (R1-1610472).
    Power is “wasted” during small info blocks decoding because of the additional hardware required to support flexibility
      Clock gating and memory powerdown do not prevent unnecessary signal activity on very long wires
   Limited energy saving when decoding small info block sizes

## Slide 5: Observations
2-code solution is more power efficient
  Internal signal activity contributes to dynamic power
    In a 2-code solution, total distance to move data is limited to smaller-area decoder
  In larger area design, data travel greater distance on longer wires
    More activity generated on longer wires
 Moving data around in an LDPC-only flexible decoder consumes more power compared to a 2-code solution

## Slide 6: Proposal
2-code solution is supported for eMBB Data Channel