## Slide 1: Way forward on observations for eMBB data channel coding
Samsung, Qualcomm Corporation, Nokia, ASB, Intel Corporation
3GPP TSG RAN WG1 Meeting #87 R1-1613341
Reno, US 14th - 18th November 2016
Agenda item: 7.1.5.1

## Slide 2: Background
Agreement:
  The channel coding scheme for eMBB data is LDPC, at least for information block size > X
  FFS until RAN1#87 one of Polar, LDPC, Turbo is supported for information block size of eMBB data <= X
    The selection will focus on all categories of observation, including overall implementation complexity, regardless of the number of coding schemes in the resulting solution (except if other factors are generally roughly equal)
  The value of X is FFS until RAN1#87, 128 <= X <= 1024 bits, taking complexity into account
  The channel coding scheme(s) for URLLC, mMTC and control channels are FFS

## Slide 3: Proposal 1
Observation 1:
  LDPC performance can be improved at small blocklengths if accounting for CRC size which normalizes false alarm rate, leading to competitive performance with Polar and Turbo codes.

## Slide 4: Background for Observation 1
Fair comparison under equal FAR (False Alarm Rate)
  LDPC:
    Inherent error detection (parity check) to detect errors.
    The required CRC bits to support similar FAR (as in LTE) is lower compared to other codes.
  Polar Code:
    The error detection of CRC aided list decoders becomes poorer with increasing list size.
    Therefore, extra CRC bits are required to provide similar error detection statistics as LTE turbo codes
  Turbo Code:
    It does not have inherent error detection and has to rely on CRC bits to detect errors
Company | Tdoc number | Observations
Ericsson | R1-1611327 | Inherent LDPC parity check sum allows LDPC codes to use fewer CRC bits than other coding candidates.
Samsung | R1-1612550 | LDPC codes usually can provide a certain level of FAR without CRC bits.
Nokia | R1-1612276 | LDPC can use inherent error detection (parity check) to detect errors.
ZTE | R1-1611109 | For LDPC code, the FAR performance of 12 bit CRC with H*CT=0 aided is superior to that of 16 bit CRC.

## Slide 5: Background for Observation 1, cont.
LDPC performs better than LTE Turbo codes and Polar codes for information block sizes below 1024 bits, when fair comparison under equal FAR is considered
Company | Tdoc number | Observations
Nokia, ASB | R1-1612276 | Considering all block sizes, LDPC shows very good performance for all code rates that are in interest for eMBB data
Samsung | R1-1612550 | When false alarm rates and decoding complexity are the same, the performance of polar codes with list-4 decoding and LDPC codes with offset MS decoding is comparable for short information block size K<1000.
R1-1612550, "Short-length LDPC Codes for NR", RAN1 #87, Samsung
R1-1613043, "Performance Comparison of Short Length LDPC and Polar Codes", RAN1 #87, Samsung
R=2/3, 3/4, 5/6, 8/9
R=1/5, 1/3, 2/5, 1/2

## Slide 6: Proposal 2
Observation 2:
  LDPC IR HARQ provides more robustness and can address diversity issues reported with Polar incremental-freezing (IF) HARQ.

## Slide 7: Background on Observation 2
LDPC IR-HARQ shows better diversity gain, adopts dynamic HARQ easily
Polar IF-HARQ has fundamental limitation from its structure, which causes increase in the complexity/latency and lacks diversity gain
Company | Tdoc number | Observations
Ericsson | R1-1611320 | To date, Polar codes do not have an effective HARQ-IR scheme considering performance and implementation
Intel | R1-1612585 | In such case, there can be some performance issues/concerns because the code diversity (or the redundancy in the retransmission) can only benefit a subset of information bits directly, and the remaining bits still have to be recovered using the first transmission.
Nokia, ASB | R1-1612278 | For eMBB, having simple IR HARQ scheme with good performance is crucial and polar does not have the support that is required to get the benefits of incremental redundancy
Qualcomm | R1-1612087 | IF based Polar-IR is substantially worse than Turbo and LDPC-IR HARQ at re-transmission due to its limitation to capture diversity across HARQ retransmissions despite its optimality over a time invariant channel
Samsung | R1-1612555 | On the EPA channels with Doppler spread 5Hz (relatively slow and flat fading), the performance of polar-IR is worse than that of LDPC-IR by 2.8dB, 7dB, 9dB at BLER = 1% in the second, the third, and the fourth retransmission, respectively.
R1-1612087, “Further evaluation of Polar HARQ”, RAN1 #87, Qualcomm Incorporated

## Slide 8: Proposal 3
Observation 3:
  LDPC performance can be improved at very small blocklengths if employing list decoders or quasi-ML decoders, leading to comparable performance with Polar and Turbo codes.
    Some of these decoding approaches may fully leverage HW used for larger blocklengths

## Slide 9: Background on Observation 3
R1-1613072, “Near optimal performance for LDPC with OSD/List decoding” RAN1 #87, Nokia, ASB, Verizon, Xilinx
Company | Tdoc number | Observations
Ericsson | R1-1611323 | For short block lengths, with quasi-ML decoding algorithms, LDPC codes have the potential to deliver comparable FER performance as other code types
Intel | R1-1612585 | Saturated MS decoder can further improve LDPC performance by ~0.5 dB at block length 104.
Nokia, ASB, Verizon, Xilinx | R1-1612277 | LDPC codes can improve their performances by assuming quasi-ML decoding algorithms, which often outperform polar and turbo due to their very good minimum Hamming distance properties.
Qualcomm | R1-1612081 | ML decoding performance of candidate channel coding schemes are comparable.
Samsung | R1-1612551 | The performance of short length LDPC codes with SMS afterburner decoder can be enhanced from a few tenth of dB to almost 1 dB SNR gain.

## Slide 10: Proposal 4
Observation 4:
  For devices which already have LDPC decoder, a second decoder for data channel can have a significant and unnecessary area and complexity impact

## Slide 11: Background on Observation 4
  A single codec solution is more efficient compared to dual codes in various aspects including energy and area efficiencies:
    Short LDPC codes can be decoded using the long LDPC decoder with negligible overhead.
    Short LDPC codes can be decoded using the long LDPC decoder in an energy efficient manner
    Having a single code allows more flexibility to optimize the decoder implementation
    Dual codes incur additional complexities in designs/operations for rate-matching, HARQ mechanisms, and so on
    Adding a second Polar decoder for short block lengths can incur extra 65% area relative to LDPC only solution (R1-1612085)
Company | Tdoc number | Observations
Intel | R1-1612585 | Supporting two coding schemes on the data channel can incur additional area impact multiple coding schemes on data path incur additional complexity on various design, rate-matching, HARQ mechanisms The two coding schemes is likely to allude to different latencies/tputs
Nokia, ASB, | R1-1612275 | Adding new code to support lower block size reduce the area efficiency of both encoder and decoder Having single code allows more flexibility to the device manufacturer to optimize the decoder implementation
Qualcomm | R1-1612085 | Using polar codes for short blocks incurs a large area overhead. Short LDPC codes can be decoded using the long LDPC decoder with negligible overhead. Short LDPC codes can be decoded using the long LDPC decoder in an energy efficient manner.
Samsung | R1-1612547 | It is very obvious that one code solution is much better than two code solution in terms of implementation complexity

## Slide 12: Background on Observation 4, cont.
Performance of Polar codes for lower code rate is poor when mother polar code block is limited to 2048, that is repetition has poor performance.
Company | Tdoc number | Observations
Nokia, ASB, | R1-1612276 | Performance of Polar codes for lower code rate is poor when mother polar code block is limited to 2048
Samsung | R1-1612552 | The length of mother polar codes are restricted to powers of two