## Slide 1: WF on NR-PBCH evaluation
NTT DOCOMO, [Qualcomm]…
3GPP TSG RAN WG1 #87 R1-1613480
Reno, USA
14th – 18th November 2016
Agenda item: 7.1.2.2
Document for decision

## Slide 2: Background
Agreements (RAN1#86):
In order for the transmission of the information required for the initial access (e.g. configuration of random access resource), at least following options are to be studied:
  Note: the above information can consist of multiple parts, and different option below can be applied for the transmission of each part
  Opt 1: the transmission is scheduled by dynamic signaling (e.g. control channel)
  Opt 2: the transmission is scheduled by semi-static signaling (e.g. via the previous part)
  Opt 3: the transmission is done alone without associated signaling (e.g. predefined in spec)
In the above study, at least following aspects should be considered:
  Resource flexibility (e.g. in terms of ensuring forward compatibility, dynamic TDD operation)
  Resource overhead
  UE complexity (e.g. involved with decoding of the information)
Agreements (RAN1#86bis):
NR defines at least one broadcast channel: NR-PBCH
  NR-PBCH decoding is based on the fixed relationship with NR-PSS and/or NR-SSS resource position irrespective of duplex mode and beam operation type at least within a given frequency range and CP overhead
    FFS: Unlicensed spectrum case
  FFS relationship between NR-PBCH subcarrier spacing and NR-PSS and/or SSS subcarrier spacing
  Following broadcasting schemes to carry essential system information can be considered
    Option 1: NR-PBCH carries a part of essential system information for initial access including information necessary for UE to receive channel carrying remaining essential system information
    Option 2: NR-PBCH carries minimum information necessary for UE to perform initial UL transmission (not limited to NR-PRACH) in addition to information in Option 1
    Option 3: NR-PBCH carries all essential system information for initial access
    Other options are not precluded
In order to decide broadcasting scheme and detailed design parameters for NR-PBCH, evaluation on NR-PBCH design parameters are necessary.

## Slide 3: Proposal
Companies are encouraged to propose and evaluate following design parameters of NR-PBCH until next meeting
  Payload size
  Overhead of PBCH (time/frequency resource amount)
  RS for demodulation, e.g., NR-SSS or dedicated DMRS or mobility RS
  Transmission scheme, e.g., MCS, transmit diversity
  Periodicity
  Resource mapping/multiplexing within SS block(s)
Following target requirements should be taken into account in the NR-PBCH design
  Detectable at low SNR condition such as [-6] dB
    Note: it does not mean NR-PBCH should be detectable by one-shot
Following can be considered
  Combining NR-PBCH across SS blocks within X ms
    FFS: Value of X ms
  Use of PBCH for finer frequency offset estimation