## Slide 1: WF on UE Capability Indication Enhancement for OTDOA Positioning in FeMTC
Nokia, Alcatel-Lucent Shanghai Bell, Ericsson, Qualcomm, Verizon
R1-1613625
3GPP TSG RAN WG1 Meeting #87
Reno, USA, 14th-18th November 2016
Agenda item 6.2.8.3

## Slide 2: Background
In RAN1#86bis meeting, it was agreed to
Support PRS frequency hopping in OTDOA for FeMTC
Study the details for multiple PRS configurations with difference PRS bandwidths
In existing LPP, the UE is able to provide its OTDOA positioning capabilities to the E-SMLC by OTDOA-ProvideCapabilities IE, where the UE capability information include
otdoa-Mode
supportedBandListEUTRA
interFreqRSTDmeasurement-r10
additionalNeighbourCellInfoList-r10

## Slide 3: Proposals
Proposal
The UE could optionally provide its capability information below for OTDOA positioning to the E-SMLC in LPP
  Maximal PRS bandwidth for RSTD measurement
    Value range: ENUMERATED { n6, n15, n25, n50, n75, n100}
  PRS-frequency-hopping-based RSTD measurement
    Value range: ENUMERATED { supported }
Example
Add the capability indication of maximal PRS bandwidth for RSTD measurement into existing OTDOA-ProvideCapabilities IE in LPP
Add the capability indication of PRS-frequency-hopping-based RSTD measurement into existing OTDOA-ProvideCapabilities IE in LPP