## Slide 1: WF on SRS
Huawei, HiSilicon, Xinwei, Samsung, ATT
3GPP TSG RAN WG1 Meeting #86bis
Reno, USA 14th - 18th November 2016
Agenda item: 7.1.3.2
R1-1613745

## Slide 2: Past Agreement
R1-1610983 WF on SRS-based UL link adaptation LG Electronics, CATT, Huawei, HiSilicon, Samsung
Agreements:
At least one of precoded and non-precoded SRS based UL link adaptation procedure should be supported in NR, with at least following different procedures:
  UL data scheduling (MCS/precoder/rank) is based on non-precoded SRS transmission by UE
    Configurable number of SRS ports are 1, 2, 4, or [8]. Other possible numbers FFS.
    FFS on precoder/codebook
  UL data scheduling (MCS/precoder/rank) is based on precoded SRS(s) transmission by UE
    Configurable number of SRS ports are 1, 2, or 4. Other possible numbers FFS.
    Multiple precoded SRS resources (if supported) can be configured.
    At least one of the following is supported
      Precoder for SRS can be determined by UE based on measurement on DL RS and
      Precoder for SRS can be indicated by gNB
    FFS on precoder/codebook
  UL data scheduling (MCS/precoder/rank) is based on a combination of non-precoded and precoded SRS transmission by UE
  Note: Some parts of above procedures might be transparent to UE
  FFS: UE may select a subset of SRS ports for SRS transmission

## Slide 3: Proposal
  If precoded SRS is supported, UL data scheduling (MCS/precoder/rank) is based on precoded SRS(s) transmission by UE
    Configurable number of SRS ports are 1, 2, or 4, or 8.
    Multiple precoded SRS resources (if supported) can be configured.
    Both of the following are supported
      Precoder for SRS can be determined by UE based on measurement on DL RS and
      Precoder for SRS can be indicated by gNB
      FFS: possibility of using both of the above
      FFS: precoder can be signaled directly or indirectly
    Note: Some parts of above procedures might be transparent to UE