## Slide 1: On spectral utilization and EVM for NR
3GPP TSG-RAN WG1 Meeting #88
Athens, Greece, 13 - 17 February, 2017
Agenda item: 8.1.5
Orange
R1-1703379

## Slide 2: background
The spectral utilization (SU) and EVM have been extensively studied for f-OFDM and Windowed Overlapped Add (WOLA).
The previous studies show that f-OFDM can achieve better SU than WOLA, e.g. for 10 MHz carrier bandwidth, f-OFDM can reach 97.2% SU [1]
WOLA can improve SU by increasing the window length [2] however this will reduce the protection for multi-path propagation [3,4]
f-OFDM can achieve better SU while having higher EVM at edge PRBs.
In this contribution, we present a spreading method that can be applied at the edge PRBs to increase the SU for WOLA, or reduce the edge EVM loss for f-OFDM
[1] R4-1609411, Further discussion on spectrum utilization, Huawei, HiSilicon
[2] R4-1609647, F-OFDM vs WOLA for Guardband, Qualcomm Incorporated
[3] NR waveform discussion , Huawei, 2017.1
[4] R4-1609945, Further elaboration on NR guard, Ericsson

## Slide 3: Study assumptions
Single numerology in downlink case, carrier bandwidth 10 MHz
Rapp PA model is considered
SE is estimated with theoretical Shannon capacity
f-OFDM with 50% filter length
WOLA with 2% window length

## Slide 4: EVM and PSD for WOLA
Pros:
  constant EVM  no edge issue
Cons:
  with 2% window, marginal SU improvement is obtained (< 1%)
Conclusion: WOLA with 2% window length can difficultly have better SU than LTE

## Slide 5: SU improvement for WOLA
Use spreading method at the edge PRBs (in green) can increase the overall SU and SE
spreading method: each modulated symbol carried on additional PRBs to reach SU higher than 90% are frequency spread on consecutive REs with spreading sequence [1,-1].
1
2
3
4
49
50
5
PRB index
53
54
51
52
a
-a
b
-b
c
-c
subcarrier index in 1 PRB of edge PRB
f
-f
1
2
3
4
5
6
11
12
spreading
method
a, b, c, …, f, are complex symbols

## Slide 6: SU improvement for WOLA
Using spreading method, the spectrum decay at edge band is proportional to 1/f^2, instead of 1/f (i.e. sinc-alike power decay)
Using spreading method at edge PRBs, the SU for WOLA with 2% window length can be increase up to 97.2%
No EVM issue

## Slide 7: SE improvement for WOLA (with 2% window length)
SE can be improved and always better than WOLA 50 PRB and f-OFDM with 54 PRB

## Slide 8: EVM improvement for f-OFDM using spreading method on additional edge PRBs
Edge EVM can be improved and no remarkable impact on SU

## Slide 9: Complexity and latency for WOLA and f-OFDM applying spreading method
complexity: almost no added complexity
latency: no impact on latency

## Slide 10: Observations and proposal
Observations
  Using spreading method at edge PRBs can improve SU for WOLA without increasing the window length
  Using spreading method at edge PRBs can improve the edge EVM for f-OFDM
  Using spreading method at edge PRBs does not impact on the complexity or latency
Proposal
  Modulated symbols carried on edge PRBs can be configured to be frequency spread on consecutive REs with spreading sequence [1,-1] either to reach SU higher than 90% or to lower EVM of the edge PRBs.

## Slide 11: Thanks