## Slide 1: WF on HARQ-ACK support for 2 HARQ processes
LG Electronics, …
3GPP TSG RAN WG1 Meeting #88
Athens, Greece, 13th -17th February 2017
Agenda item 7.2.4.3
R1-1703552

## Slide 2: Background
HARQ-ACK feedback with existing individual HARQ-ACK timing for DL 2 HARQ processes can lead to the serious collision issue between
  Two NPUSCH Format 2 carrying HARQ-ACK responses, or
  NPUSCH Format 2 carrying HARQ-ACK response and NPDSCH (Table below shows scheduling restriction to the NSF and NRep values to avoid the collision)

## Slide 3: Proposal 1
When a NB-IoT UE is configured with 2 HARQ processes, the following collision cases should be handled regarding the transmission of HARQ responses for two HARQ processes:
  when the HACK-ACK transmission timing for the first scheduled NPDSCH partially or fully overlaps with the second scheduled NPDSCH
  when the HARQ-ACK transmission timings for the first scheduled NPDSCH and the second scheduled NPDSCH partially or fully overlap.

## Slide 4: Proposal 2
When a NB-IoT UE is configured with 2 HARQ processes operation, the UE transmits two bits HARQ-ACK responses for the scheduled two NPDSCHs with different HARQ process IDs by QPSK constellation on the HARQ-ACK resource corresponding to the second NPDSCH in the following cases:
  when the HACK-ACK transmission timing for the first scheduled NPDSCH partially or fully overlaps with the second scheduled NPDSCH
  when the HARQ-ACK transmission timings for the first scheduled NPDSCH and the second scheduled NPDSCH partially or fully overlap.
QPSK modulation for the HARQ-ACK responses for two HARQ processes follow the table below, where b(i) indicates the first scheduled NPDSCH and b(i+1) indicates the second scheduled NPDSCH

## Slide 5: Example
NACK-to-ACK error due to missing NPDCCH cases can be avoided with the proposal