## Slide 1: Proposal on RSRP threshold offset for reduced power class NB-IoT UEs
LG Electronics, NTT DOCOMO, …
3GPP TSG RAN WG1 Meeting #88
Athens, Greece, 13th -17th February 2017
Agenda item 7.2.4.5
R1-1703553

## Slide 2: Background
In RAN2#96, RAN2 decided the following.
  UE with reduced power class shall correct the RSRP threshold (signalled in the NPRACH configuration) with (P-23) (P = power of the reduced power class UE)
According to the decision, 14dBm capable NB-IoT UE will always applies 9dB offset to the RSRP threshold for the initial CE level decision, which results in unnecessary preamble repetitions for 14dBm capable NB-IoT UEs compared to the 23dBm capable UEs if the network set PEMAX,c value smaller than 23 dBm so that the RSRP threshold is set assuming maximum transmission power smaller than 23dBm even for 23dBm capable NB-IoT UEs.

## Slide 3: Proposal
Modify the current RAN2 decision regarding RSRP threshold offset as follows and inform RAN2 of the decision.
  UE with reduced power class shall correct the RSRP threshold (signalled in the NPRACH configuration) with (P-23) min{0, (P-min(23, PEMAX,c))} (P = power of the reduced power class UE)