## Slide 1: WF on UL signal for link failure recovery request
LG Electronics, Huawei, HiSilicon, MediaTek, Samsung, Nokia
R1-1703571
3GPP TSG RAN1 meeting #88
Athens, Greece, Feb. 13 – 17, 2017
Agenda Item: 8.1.2.2.2

## Slide 2: Background
Agreements in RAN1 Ad-Hoc meeting
  NR supports that UE can trigger mechanism to recover from beam failure
  Network explicitly configures to UE with resources for UL transmission of signals for recovery purpose
    Support configurations of resources where the base station is listening from all or partial directions, e.g., random access region
  FFS: Triggering condition of recovery signal (FFS new or existing signals) associated UE behavior of monitoring RS/control channel/data channel
  Support transmission of DL signal for allowing the UE to monitor the beams for identifying new potential beams
    FFS: Transmission of a beam swept control channel is not precluded
    This mechanism(s) should consider tradeoff between performance and DL signaling overhead

## Slide 3: Proposal
At least one of following alternatives for beam recovery should be supported
  The UL signal to report beam recovery at least can be located in the same slot as PRACH.
    Alt1. Part of the PRACH sequence resource is used for beam recovery purpose.
    Alt2. Resources that is orthogonal to PRACH resources is used for beam recovery purpose
  FFS: The UL signal located at a slot different from PRACH
    Consider the impact of RACH periodicity in configuring the UL signal to report beam recovery located in slots outside PRACH
  Other channels/signals for beam recovery are not precluded (e.g., SR, UL grant free PUSCH, UL control)