## Slide 1: WF on resource allocation for PDSCH with wider channel bandwidth
ZTE, ZTE Microelectronics, …
3GPP TSG RAN WG1 Meeting #88 R1-1703574
Athens, Greece 13th - 17th February 2017
Agenda Item: 7.2.3.1.1

## Slide 2: Background
The following agreements were achieved in RAN1 #87 meeting:
  For Rel-14 BL/CE UE configured with max 5 MHz PDSCH channel bandwidth, contiguous and non-contiguous resource allocation is supported
  For Rel-14 non-BL UEs configured with max 20 MHz PDSCH channel bandwidth, contiguous and non-contiguous resource allocation is supported

## Slide 3: Observations -1
Overlapped DL wideband definition can be used to achieve higher scheduling flexibility in CE mode A.
Overlapped wideband can be indicated by ‘Starting narrowband index’.
10 MHz
15 MHz
20 MHz

## Slide 4: Observations - 2
In CE mode B, keeping the resource allocation overhead for larger channel bandwidth same as 1.4 MHz case is beneficial for coverage enhancement.
To reduce the DCI overhead, ‘Wideband index’ can be used to indicate non-overlapped wideband in CE mode B.
10 MHz
15 MHz
20 MHz

## Slide 5: Proposal -1
For resource allocation of Rel-14 BL/non-BL UE configured with PDSCH with max 5 MHz channel bandwidth in CE mode A,
    ‘Starting narrowband index’ is used to indicate the overlapped wideband.
    ‘narrowband bitmap within the wideband + resource allocation within the narrowband’ is used to indicate the resource allocation within the wideband.

## Slide 6: Proposal - 2
For resource allocation of Rel-14 BL/non-BL UE configured with PDSCH with max 5 MHz channel bandwidth in CE mode B,
    ‘Wideband index’ is used to indicate the wideband.
    Resource allocation granularity is narrowband
    Narrowband bitmap within the wideband is used to indicate the resource allocation within the wideband.

## Slide 7: Proposal - 3
Resource allocation for Rel-14 non-BL UE configured with PDSCH with max 20 MHz channel bandwidth in CE mode B is based on ‘Allocated widebands’ + ‘resource allocation within each allocated wideband'
    Resource allocation within each allocated wideband can reuse max 5 MHz case in CE mode B.