## Slide 1: WF on TBS for non-BL UE in FeMTC
Ericsson, Intel, Nokia, ZTE, NTT DOCOMO, Kyocera
3GPP TSG-RAN WG1 Meeting #88 R1-1703597
Athens, Greece, 13th – 17th February 2017 Agenda Item: 7.2.3.1.2

## Slide 2: Proposal
Change the agreement on maximum TBS for a Rel-14 non-BL UE configured in CE mode A to 27376 bits.
Use existing Table 7.1.7.2.1-1 in 36.213 for determining modulation format and TBS for a non-BL UEs configured in CE mode A or B, with applicable restrictions:
  NPRB <=96 for 20 MHz BW.
    When operating in 10 MHz and 15 MHz system BW, NPRB further restricted according to the applicable allocation constraints.
  ITBS <=14 for CE Mode A and ITBS <=9 for CE Mode B