## Slide 1: WF on diversity transmission for uplink
NTT DOCOMO, Intel, Samsung, Mitsubishi Electric, Qualcomm, …
R1-1703683
3GPP TSG RAN WG1 Meeting #88
Athens, Greece 13th – 17th February 2017
Agenda item 8.1.2.1.5

## Slide 2: Backgrounds
Agreements:
Support at least the following UL transmission schemes for data in NR
  Scheme A: Codebook based UL transmission
    Support frequency selective precoding for CP-OFDM when the number of transmission port is greater than X (FFS: Value of X).
    Study codebook design including single-stage and multi-stage, e.g., W1W2 structure, codebook
    Study the following DL signaling, e.g.,
      One level DCI
      Two level DCI
      MAC CE
      DCI associated with PDSCH (like UCI associated with PUSCH in LTE)
  Scheme B: Non-codebook based UL transmission
    Support frequency selective precoding for CP-OFDM when the number of transmission port is greater than Y (FFS: Value of Y).
    Support the indication of DL measurement RS for UE to calculate candidate precoder
    Study the mechanisms for UL precoder determination, e.g. precoded SRS based, non-precoded SRS based, hybrid precoded and non-precoded SRS based
  Diversity-based transmission schemes
    FFS: Whether the scheme has specification impact or not
  FFS: Merging of the schemes
Support rank determination by gNB
Support PRB bundling for CP-OFDM
  Study configurability of PRG size for CP-OFDM
  Study the PRG size
FFS: Single port transmission is supported for the UE capable for multiple antenna port transmission.

## Slide 3: Proposals
For CP-OFDM, UL transmission schemes should be based on DL transmit diversity schemes.
  If needed further down selection can be done.
For DFT-S-OFDM, following schemes can be candidates: CDD, precoder cycling, antenna port switching, SFBC and STBC.
  RAN1 should down select them in WI phase.