## Slide 1: WF on NR-SS default parameters
NTT DOCOMO
3GPP TSG RAN WG1 Meeting #88 R1-1703700
Athens, Greece
13th – 17th February 2017
Agenda item: 8.1.1.1.1
Document for decision

## Slide 2: Background
Working assumptions:
About 1000 hypotheses provided by NR-PSS/SSS to represent NR physical cell ID for NR-SS design
  FFS whether NR-PSS/SSS could be used to indicate information other than NR physical cell ID
  FFS further extension of ID space for non-mobility purpose through e.g., broadcast
RAN1 considers NR-PSS and NR-SSS have same transmission bandwidth
Possible agreements:
RAN1 considers following categories to define set of NR-SS design parameters
  Frequency range category #A associated with minimum carrier bandwidth of 5 MHz
  Frequency range category #B associated with minimum carrier bandwidth of [10] MHz
  Frequency range category #C associated with minimum carrier bandwidth of [40 or 80] MHz
RAN1 considers following sets of default subcarrier spacing for NR-PSS/SSS
  For frequency range category #A, 15 kHz subcarrier spacing
  For frequency range category #B, 15 kHz and 30 kHz subcarrier spacing
  For frequency range category #C, 120 kHz and 240 kHz subcarrier spacing
  Note that association between a frequency band and single set of default parameters (SCS, sequence length, NR-SS transmission bandwidth) will be defined in RAN4
  Note that each subcarrier spacing is associated with single sequence length and transmission bandwidth
  FFS further down selection if necessary
RAN1 sends LS to RAN4 to inform above RAN1 considerations

## Slide 3: Proposal
RAN1 considers following categories with associated default subcarrier spacing and possible maximum transmission bandwidth for NR-SS design
  Frequency range category #W associated with 15 kHz subcarrier spacing and NR-SS transmission bandwidth no larger than 5 MHz
  Frequency range category #X associated with 30 kHz subcarrier spacing and NR-SS transmission bandwidth no larger than 10 MHz
  Frequency range category #Y associated with 120 kHz subcarrier spacing and NR-SS transmission bandwidth no larger than 40 MHz
  Frequency range category #Z associated with 240 kHz subcarrier spacing and NR-SS transmission bandwidth no larger than 80 MHz
  Note that association between a frequency band and single set of default parameters (SCS, sequence length, NR-SS transmission bandwidth) will be defined in RAN4
  Note that each subcarrier spacing is associated with single sequence length and transmission bandwidth
  Note that additional frequency range category or further down selection of frequency range category is not precluded