## Slide 1: Way forward on the order of PUSCH grants For: Decision AI: 7.1.2
Intel, Qualcomm, MediaTek, WILUS
3GPP TSG-RAN WG1 #88 R1-1703777
Athens, Greece, 13th – 17th February 2017

## Slide 2: Background
With the introduction of flexible timing scheduling and the two-stage grant, it is possible that the order of PUSCH transmission is not necessarily the same with the order of the UL grants received.
However, the legacy UE implementation assumption is that the PUSCH is always transmitted in the order of UL grants received.
This situation requires additional memory planning, to modify the current UE Tx buffer control mechanism, and consequently a lot of additional verification work.

## Slide 3: Proposal
eLAA UE is not expected to receive UL grants scheduling PUSCH earlier in time than the PUSCH scheduled by previously received UL grants.
  If a UE receives a UL grant indicating PUSCH transmission in out-of-order, the UE is not required to transmit the corresponding PUSCH.