## Slide 1: WF on PUCCH CSI feedback in advanced CSI
Huawei, HiSilicon, CATT
3GPP TSG RAN WG1 Meeting#88 R1-1703809
Athens, Greece 13th - 17th February 2017
Agenda item - 7.2.2.6

## Slide 2: Background
Advanced CSI codebook outperforms Rel-13 codebook by providing more accurate quantized precoding vector(s).
On RAN1# 87 meeting, working assumption for advanced CSI is to support both PUCCH and PUSCH CSI feedback.

## Slide 3: Proposal
Support PUCCH mode 2-1, which includes 3 reporting instances
  Report1:
    RI+PTI
  Report2:
    PTI=0: Subsampled i1(or i1,1, i1,2) for rank1/2, and i1 (or i1,1, i1,2) for rank≥3
    PTI=1: Wideband CQI + subsampled wideband i2 for rank2, and i2 for rank1 and rank≥3
  Report3:
    PTI=0: Wideband CQI + wideband i2
    PTI=1: Subband CQI + subband i2+subband label
    Report1 and report2 are carried on PUCCH format2, and report3 is carried on PUCCH format3

## Slide 4: Codebook subsampling
For i1, or i1,1 and i1,2
  When N=12 ports, (O1, O2) = (4,2)
  When N≥16 ports, (O1, O2) = (2,2)
  Otherwise, (O1, O2) = (4,4)
For i2,
  For rank2:

## Slide 5: CSI and HARQ-ACK collision
For report1/2 in PUCCH mode 2-1
  Reuse existing collision handling mechanism
For report3 in PUCCH mode 2-1,
  the UE shall drop the CSI and transmit the HARQ-ACK or SR (if existing) on HARQ-ACK resource.