## Slide 1: WF on PRB Bundling in NR Uplink
Samsung, CATT, Qualcomm, Interdigital
3GPP TSG RAN WG1 #88 Meeting draft R1-1703908
Athens, Greece, Feb 13-17, 2017
Agenda item: 8.1.2.1

## Slide 2: Background on PRB bundling in UL
PRBs can be grouped into PRGs where UE will apply same precoder in all PRBs of a PRG
Can improve DMRS based channel estimation
  Less edge effect degradation
  Large processing gain
PRB bundling can improve channel estimation at gNBs, but large PRG size can lead to higher receiver complexity.
PRB bundling may be turned on and off efficiently based on the configuration.
  For example: in the case of frequency selective precoding in reciprocity calibrated UEs, it may be beneficial not to use PRB bundling.
  Different transmission configuration requires different PRB bundling configurations.

## Slide 3: Background on PRB bundling in UL
Agreement in RAN1-#87
  Study further the PRB bundling size for UL data
    DFT-S-OFDM based transmissions
      Consider the case of contiguous scheduled PRBs and non-contiguous scheduled PRBs (if supported)
      Consider the impact due to UL DM-RS design
    CP-OFDM based transmissions
      Considering aspects related to non-reciprocity based CP-OFDM transmission (if supported) and reciprocity based CP-OFDM transmission (if supported)
Agreement in RAN1-NR-1 (Spokane)
  Support PRB bundling for CP-OFDM
    Study configurability of PRG size for CP-OFDM
    Study the PRG size

## Slide 4: Proposal
For DFT-S-OFDM based transmission
  PRG size is the whole scheduled bandwidth if the scheduled bandwidth comprises a single cluster.
    Note: UE shall apply the precoder in a way that the gNB may assume that UE uses the same precoder for all scheduled PRBs.
  Multi cluster case FFS (if supported)
CP-OFDM based transmission
  Non-reciprocity based CP-OFDM transmission (if supported) (TPMI based transmission),
    PRB Bundling should be supported.
    PRG size implicit determination
      FFS: available schemes.
  Reciprocity based CP-OFDM transmission (if supported) (UEs are allowed to choose precoder by themselves)
    FFS: Configurability by gNB side e.g.
      PRB bundling on or off.
      PRG size.