## Slide 1
3GPP TSG RAN WG1 Meeting #88 R1-1704047
Athens, Greece, 13th - 17th February 2017
Agenda item: 8.1.2.4.2
WF on NR DM-RS Configuration
Nokia, ASB, Samsung, NTT DOCOMO, ZTE, ZTE Microelectronics, CATT, MediaTek

## Slide 2: Proposals
NR supports at most N DMRS configurations for CP-OFDM, for a given number of antenna ports
  FFS: N
  FFS: DMRS configurations for DFT-s-OFDM
  Note that DMRS configuration can includes DMRS pattern, DMRS position, multiplexing scheme etc (Other parameters are not precluded. )
  NR DMRS supports the frequency domain configurations considering following aspects
    DMRS overhead reduction
    Improving channel estimation performance
  NR DMRS supports the time domain configurations for following scenarios
    Low mobility and Low latency scenario (e.g. up to ~30km/h),
    Medium/high mobility scenario (e.g. up to ~ 250km/h)
    Very high mobility scenario(e.g. up to ~500km/h)
    Note: Low latency scenario is not expected for high mobility scenario
    FFS: whether or not each scenario can have more than one configurations.